## Slide 1: Losses of energy in pipes
When fluid flow through pipes, the fluid experiences some resistance due to which energy of fluid is lost.
This losses is classified in two parts Major Losses & Minor Losses

## Slide 2: Energy losses
Energy Losses
Major Losses
Minor Losses

## Slide 3: Major Losses
This is due to friction and calculated by following formulas:
1. Darcy- Weisbach Formula:
hf = (4.f.L.V2 )/(d.2g)
where
hf = Coefficient of friction (function of Reynolds's Number)
f = Friction Factor
= 16/Re Re< 2000 (Viscous Flow)
= 0.079/(Re)1/4 4000<Re< 106
Re = (ρVd)/μ or (Vd)/ν ρ = density μ = dynamic viscosity
ν = kinematic viscosity
L = length of pipe
V = mean velocity of flow
d = diameter of Pipe
g = acceleration due to gravity (9.8 m/s2)
2. Chezy’s Formula:
V= C√(mi)
V = mean velocity of flow
m = hydraulic mean depth
= A (area of flow)/ P ( wetted perimeter)
= d/4 (in case of pipe)
i = loss of head per unit length of pipe (hf /L)
C = Chezy’s constant

## Slide 4
Numerical:
Q1.Find the head loss due to friction in a pipe of diameter 250 mm & length 60m, through which water is flowing at a velocity of 3.0 m/s using (i) Darcy formula (ii) Chezy’s formula for which C = 55 . Take kinematic viscosity of water ν = 0.01 stokes
Q2. Find the diameter of pipe of length 2500m when the rate of flow of water is 0.25m3/s and head lost due to friction is 5 m Take C= 50 in Chezy’s formula.
Q3. An oil of kinematic viscosity 0.25 stokes is flowing through a pipe of diameter 300 mm at a rate of 300 litre/s . Find the head lost due to friction for a length of 60 m of pipe.
Q4. An oil of specific gravity 0.7 is flowing through a pipe of diameter 300 mm at the rate of 500 liters/s. Find the head lost due to friction and power required to maintain the flow for a length of 1000m. Take ν = 0.29 stokes